## Slide 1
Audio Voice Over Circuit
The audio voice-over circuit is designed to effortlessly alternate between two audio sources, typically a microphone input and an external audio input, based on user desire. It guarantees higher sound quality with minimum noise, distortion, and latency.

## Slide 2
Audio Voice Over Circuit

## Slide 3
Bandpass-Filter
  Used NE5532P IC containing two op-amps to build a bandpass filter.
  Designed to reduce echo feedback from the microphone input.
  Filter isolates the frequency range of 500-5000 Hz.
  Ensures clear audio output by minimizing unwanted feedback and preserving signal quality.

## Slide 4
Pre-Amplifier
  Band-Pass filter output drives through a pre-amplifier.

## Slide 5
Peak-Detector
  Utilized a NE5532P IC.
  Circuit captures the peak amplitude of the input audio signal.
  Provides a steady DC output proportional to the peak amplitude.
  Output serves as the input to the comparator for threshold detection.

## Slide 6
Comparator
  Used another NE5532P IC.
  Comparator compares the peak detector’s output with a predefined threshold voltage.
  Generates a high output when the peak signal exceeds the threshold.

## Slide 7
Switching-Circuit
  Employed a 2N3904 NPN transistor and a relay.
  Comparator's output acts as the control signal for the circuit.
  Transistor output drives the relay.
  Ensures efficient signal routing between,
  microphone input
  audio input.

## Slide 8
Main-Amplifier
  Used the LM386N IC to build an audio amplifier.
  Designed to boost the signal strength for audio applications.
  Provides sufficient gain and output power for clear sound.
  Amplifies the input audio signal effectively.
  Ensures compactness and energy efficiency in the overall design.

## Slide 10
PCB Design

## Slide 11
Enclosure

## Slide 13
Thank you!!!
  Bandara.I.W.T.N 220061H
  Wijenayaka.M.B.T.I 220711D
  Senaweera.S.A.H.D 220596C
  Sanjeewa.P.M.G.P.N 220577U
Team Syncronix,